## Slide 1
AGRIBOT
ADVANCE MOBILE PHONE OPERATED MULTI PURPOSE AGRICULTURE ROBOTIC VEHICLE
GUIDE:
Mrs.N.Krishna Jyothi
Asst. Professor
Department of ECE
Batch C3:
Arisetty Sri Ramani (19251A04C3)
Gottipati Ashlesha (19251A04D2)
Manchina Roshini (19251A04E4)
Vanama Sahithi Jayaram (19251A04J0)

## Slide 2
CONTENTS
  INTRODUCTION
  HARDWARE AND SOFTWARE REQUIREMENTS
  BLOCK DIAGRAM
  WORKING PRINCIPLE
  ADVANTAGES and DISADVANTAGES
  APPLICATIONS
  KIT
  RESULTS
  CONCLUSION AND FUTURE SCOPE

## Slide 3
  Agriculture is the backbone of India.
  Some of the major problems in the Indian agricultural are rising of input costs, availability of skilled labors, lack of water resources and crop monitoring.
  To overcome these problems, the automation technologies were used in agriculture.
  The model development and the fabrication of the robot these whole systems of the robot works with the battery and power supply.
INTRODUCTION

## Slide 4
OBJECTIVES
  To check the moisture content and taking necessary actions.
  To plough the soil and cut the unwanted grass.
  To help the farmers in ploughing.
  To sow seeds.
  To send update messages to farmer's mobile.

## Slide 5
  Arduino UNO
  RPS (12V)
  Humidity/ Soil Moisture Sensor
  L293D Driver IC
  DC Motors
  Orcad Design
  GSM module
HARDWARE REQUIREMENTS

## Slide 6
SOFTWARE REQUIREMENTS
  Arduino UNO
  Software serial GPRS for Arduino

## Slide 7
  The Atmel AVR core combines a rich instruction set with 32 general-purpose working registers.
  The ATmega328/P is supported with a full suite of program and system development tools including C Compilers, Macro Assemblers, Program Debugger/Simulators, In-Circuit Emulators, and Evaluation kits.
  All 32 registers are directly connected to the Arithmetic Logic Unit
ARDUINO UNO

## Slide 8
  The Moisture sensor is used to measure the water content (moisture) of soil.
  When the soil is having water shortage, the module output is at high level; else the output is at low level.
MOISTURE SENSOR
WATER MOTOR
  This is a low cost, small size Submersible Pump Motor which can be operated from a 3 ~ 6V power supply.
  It can take up to 120 liters per hour with very low current consumption of 220mA.

## Slide 9
  GSM is a cellular network, which means that mobile phones connect to it by searching for cells in the immediate vicinity.
  .GSM-900 uses 890–915 MHz to send information from the mobile station to the base station (uplink) and 935–960 MHz for the other direction.
  Time division multiplexing is used to allow eight full-rate or sixteen half-rate speech channels per radio frequency channel.
GSM MODULE

## Slide 10
  A dc motor uses electrical energy to produce mechanical energy, very generally through the interaction of magnetic fields and current-containing conductors.
  The DC motor has two basic parts: the rotating part that is called the armature and the stable part that includes coils of wire called the field coils.
DC MOTOR

## Slide 11
BLOCK DIAGRAM

## Slide 12
  The basic idea of this project is to develop a multipurpose machine, which is used for ploughing the soil, and water sprayer to spray water with least changes in accessories with minimum cost.
  This whole system of the robot works with the battery and the solar power.
  Robot has rotor which will destroy the unwanted grasses while moving and also level the ground.
  All the operations are performed with the help of PIC microcontroller.
  Humidity sensor is used to sense the moisture content in the environment.
WORKING PRINCIPLE

## Slide 13
  Moisture sensor is used to sense the water level in the ground and turn on and turn off the pumping motor depending on water level.
  The GSM module is used to send the update messages to the user about the functioning of the robot.
  The robot is also used for seed sowing by digging the soil at certain intervals and placing the seeds inside, and closing the soil.
.
WORKING PRINCIPLE CONTD.

## Slide 14
  Reduces the number of labors required for agricultural activity.
  Due to its quick action, time will be saved.
  Agribot can able to work in any environmental condition.
  The robots can work without sleep so they can work 24*7 for 365 days.
  Protection against harmful effects of chemicals.
ADVANTAGES

## Slide 15
DISADVANTAGES
  As machines will do all the work there will be less scope for employment of labor mainly in rural villages.
  Robot needs high maintenance.
  In a way or other emotional appeal of agriculture may be changed.

## Slide 16
APPLICATIONS
  Robot has rotor which will destroy the unwanted grasses while moving and also level the ground.
  The robot also has a digger to dig the vegetables from the ground.
  The robot automatically turn on and turn off of water pumping motor.

## Slide 17
KIT

## Slide 18
RESULTS

## Slide 19
  As ever increasing of world population and decreasing of agricultural workers created constraint to framing system.
  Agricultural robot has potential to take off load of labor shortage and increasing the productivity.
  Some activities like small scale irrigation, crop monitoring and seed sowing have been implemented so far.
  The system can further modified for picking fruits, and actual cutting process by the system.
CONCLUSION AND FUTURE SCOPE

## Slide 20
  Shibusawa, S. 1996. PhytoTechnology - An introduction to the concept and topic of a new Project. http://phytech.ishikawa?c.ac.jp/WhatIs.html.
  Tillett, N.D., Hague, T. and Marchant, J.A.(1998) A robotic system for plant scale husbandry. Journal of Agricultural Engineering Research, 69, 169-178.
  Blackmore, S. (2007). A systems view of agricultural robotics. Precision Agriculture conference, Wageningen Academic Publishers, the Netherlands. pp. 23-31
REFERENCES

## Slide 21
Thank You